Possible SPS experiments to test crystal collimation for LHC

By W. Scandale

2/2/2006

Abstract: We recently suggested using short bent crystals as primary collimators in a two stage cleaning system for hadron colliders, with the aim of providing larger impact parameters in the secondary bulk absorber, through coherent beam-halo deflection. Tests with crystals a few mm long, performed with 70 GeV proton beams at IEHP in Protvino, showed a channeling efficiency exceeding 85 %. We also observed disturbing phenomena such as dechanneling at large impact angle, insufficient bending induced by volume capture inside the crystal, multiple scattering of non-channeled protons and, for the first time, a proton flux reflected by the crystalline planes.

The proposed experiments in the SPS should contribute consolidating our knowledge on channeling and dechanneling phenomena and will provide a test bed for crystals to be eventually used in the LHC collimation system.