## Slide 1
High Energy Astrophysical Cherenkov Neutrino Telescope at CapoPassero: status report
Outlook
Physics with deep under-water/ice Neutrino Telescopes
Current projects in Mediterranean Sea:
  ANTARES
  NEMO
  NESTOR
Aiming at Km3 Neutrino Telescope in Mediterranean Sea:
  KM3NeT
    Joining efforts, design and technologies towards a common project
    Pan-European coordination of funding agencies and research Institutions
Status and perspectives
  KM3NeT-Italy, Km3

## Slide 2
The Universe is transparent for UHE neutrinos !
Observed elementary particles or nuclei carrying a kinetic energy up to 1021eV (like a tennis ball moving at ~150km/h)
Many open questions:
  Where they come from ?
  Which acceleration mechanism ?
  …
UHE astrophysical neutrinos will extend the limits of the "visible" Universe.
Our present knowledge about Cosmic Rays
Flux [particles/(m2 s sr GeV)]
Energy [eV]
Gamma rays (0.01 - 1 Mpc)
1 parsec (pc) = 3.26 light years (ly)
AGN, SNR, Microquasars, …
protons E<1019 eV
neutrinos
Cosmic accelerator
protons E>1019 eV (10 Mpc)

## Slide 3
A synoptic view of neutrino fluxes

## Slide 4: Detection principle
Neutrinos from cosmic sources
induce 1-100 muon evts/y
in a km3 Neutrino Telescope
Up-going µ from neutrinos
generated in atm. showers
S/N ~ 10-4
Down-going µ from atm. showers
S/N ~ 10-6 at 3500m w.e. depth
p, nuclei
p, nuclei
Atmospheric neutrino flux ~ E-3
Neutrinos flux from cosmic sources ~ E-2
  Search for neutrinos with E>110 TeV
~TeV muons propagate in water for several km
before being stopped
  go deep to reduce down-going atmospheric µ backg.
  long µ tracks allow good angular reconstruction
Picture from ANTARES
up-going neutrino
µ and induced Cherenkov cone
µ direction reconstructed from the arrival time of Cherenkov photons on the Optical Modules: needed good measurement of PMT hits, (t)~1ns, and good knowledge of PMT positions ( ~10cm)
Cherenkov
Neutrino
Telescope
Search for neutrino induced events, mainly , deep underwater
43°

## Slide 5: Our Detector concept: a 3D semi-rigid structure holding O.M. in fixed positions

## Slide 6: Point like cosmic Neutrino Sources
Galactic
Pulsar Wind Nebula
Supernova Remnants
RX J1713.73946HESS
Microquasars
Extragalactic
Active Galactic Nuclei
Their identification requires a detector with accurate angular reconstruction
Experimental signal : statistical evidence of an excess of events coming from the same direction
GRB 990123
For transient sources the time meas.
improves the signal detection

## Slide 7: An example: the ANTARES search for point-like sources

## Slide 8: Diffuse Cosmic Neutrino Sources
Unresolved AGN
Neutrinos from "Z-bursts"
Neutrinos from "GZK like" p-CMB interactions
Neutrinos foreseen by Top-Down models
….
Their identification out of the more intense background of atmospheric neutrinos (and muons) is possible at very high energies (E > TeV) and implies accurate energy reconstruction.
Search here !!!
ANTARES 2011

## Slide 9: Two VHE neutrino events observed by IceCUBE
T. Stanev
NOW-2012

## Slide 10: … not only neutrino astrophysics…
… also open problems in particle physics …
  Dark Matter searches:
    Neutralinos from Sun, Earth, Galactic Center
  Monopoles, Nuclearites
  Acceleration mechanisms
  Neutrino interactions Cross sections
  …
Neutralino search:  → +…

## Slide 11: The Neutrino Telescope World Map
ANTARES + NEMO + NESTOR joined their efforts to prepare a km3-scale Cherenkov neutrino telescope in the Mediterranean KM3NeT Consortium

## Slide 12: Locations for Neutrino Astronomy
Mkn 501
RX J1713.7-39
GX339-4
SS433
CRAB
Galactic
Centre
VELA
Mkn 501
Mkn 421
CRAB
SS433
From Antartica
From Mediterranean Sea
A Km3 Neutrino Telescope in Mediterranean Sea will be complementary to IceCube and … will search for neutrino sources in the Galactic centre
Mediterranean location provides a 3π sr sky coverage, 0.5π sr instantaneous common view with IceCube, and about 1.5π sr common view per day. The Galactic centre is visible 2/3 of the time.

## Slide 13: Mediterranean Sea  Telescope Sky Coverage
Observed sky, in galactic coordinates, by a detector efficient to tracks from below the horizon (up-going tracks).
→ We need a km3 Northern n Telescope to cover the Galactic Plane
Mediterranean site:
>75% visibility
>25% visibility

## Slide 14
International consortium involving more than 300 scientists from 10 EU countries (CY, DE, ES, FR, GR, IE, IT, NL, RO, UK)
Common objective: build the most sensitive high energy neutrino telescope in the Northern Hemisphere
KM3NeT is on the ESFRI roadmap since 2006
KM3NeT

## Slide 15
Started in February 2006 with the Design Study project co-funded with 9 M€ under the 6th EC Framework Programme
  Coordinated by University of Erlangen, Germany (U. Katz)
In 2007 included in the roadmap of the European Strategy Forum of Research Infrastructures (ESFRI)
In 2008 co-funded with 5 M€ for a “Preparatory Phase” under the 7th EC Framework Programme and concluded in february 2012
  Coordinated by INFN-LNS, Italy (E. Migneco)
A Brief History of KM3NeT

## Slide 16
March 2012: KM3NeT-PP ends, TDR released
DU technologies in the TDR
  Towers (like NEMO) + OM multi-PMTs : DOMBARS, preferred solution
  Strings + OM multi-PMTs
Funding
  FR: for sea/shore infrastr. and DUs in Toulon
  IT: for sea/shore infrastr. and DUs in Capo Passero
  NL: for Dus and DU-production site in Amsterdam
Transition to a Collaboration in preparation
A Brief History of KM3NeT – near past

## Slide 17
The String Technology
Detection Unit with 20 storeys
40 m inter-storey distance
Compact deployment
Digital Optical Module
Many small PMTs in one glass sphere
Photon counting
17
MANTS Bologna, October 6 2012

## Slide 18
KM3NeT-DU Septembre 2011
13.09.2011

## Slide 19
End of 2011
  IT: 20.8 M€ PON budget for detector construction to be spent before end 2014. Need to define the DU technology
June 2012
  Base technology for KM3NeT: the string with OM made by multi-PMTs. But this technology is not still fully proved.
  INFN will start the construction 8 TOWERS equipped by large area single PMT at Capo Passero site
  INFN will build the deep sea infrastructure capable to host Towers and Strings
The validation program of the string-DU has been resumed by the whole KM3NeT Consortium
  If by middle 2013 the string-project will have been validated INFN will switch the production to strings and KM3NeT Europe will construct and install, in Capo Passero site, as many strings as the ones built by INFN
A Brief History of KM3NeT – today

## Slide 20
The PON project, funded with 20.8M€, foresees, for the end of 2014, the construction of the first block of DUs (up to 30) at Capo Passero site:
At present (November 2012):
NEMO-Phase2 Tower ready to be deployed
The NEMO-Phase2 project has been scrutinized in order to update “old” technological solutions (when needed)
Next future:
  already started and on-going
technology transfer to industry
industrialization of the detector elements production
  December 2012
start the construction and the integration of Km3 DUs for Capo Passero
The construction of the first Detection Units of the Neutrino Telescope is now possible and it is started !

## Slide 21
Chart: 
| Bari | Bologna | LNS | CT | Genova | LNF | Napoli | Pisa | Roma | Salerno
 | 3 | 10 | 20 | 10 | 4 | 3 | 8 | 10 | 9 | 2
2013 Km3, Italian, Collaboration composition
During the last 15 years a great effort has been done by INFN for the construction of the High Energy Underwater Cherenkov Neutrino Telescope: NEMO, ANTARES, KM3NeT
2013  Km3 will include all INFN activities in this field

## Slide 22: Sensitivity at 90% C.L. for 30 Towers at Capo Passero
ANTARES, Neutrino 2012
IceCube, ICRC 2011
KM3NeT_Italy 30 Towers
130m distance between DU
20 floors
40m distance between floors
At declination -60° the KM3NeT-Italy sensitivity is 8 times larger than ANTARES
ANTARES
KM3NeT_Italy
IceCube

## Slide 23
Status of the NEMO tower validation
      Integration
      Tests
      Improvements
      Deployment program

## Slide 24
The ‘NEMO-Phase2’ tower
8 floors in Al bars
8 m length
Vertical distance of the floors = 40 m
Total height = 450 m
4 Optical Modules on each floor : 32 OMs
hydrophones+ oceanographic instruments
Acoustic & laser beacon
A validation structure for the production of the 8 initial Km3 Towers

## Slide 25
The optical module
Very simple fixation system
2 looking horizontally, 2 looking down
Glass sphere: 13’’Ø
m metal cage
Optical gel
1 LED looking to the upper floor
    Porfido: temperature RFID sensor
the Optical Module
PMT:
10 stages 10’’ Hamamatsu R7081
TTs =2.8 ns FWHM
Dark count rate ~ 1.3 kHz
After pulse ~4%

## Slide 26
4 Al tubes 8m long.
1 central vessel to host electronics
1 break out of the backbone
cables for unfolding
almost neutral in water
the top buoy
the floor
2 hydrophones Smid TR401 in floor 1-6
2 hydrophones LTD SX 30 in floor 7 (Valencia, Gandia)
2 hydrofphones custom from Erlangenin floor 8
1 C-Star in floor 4
1Doppler current sens. in floor 5
2 CTD in floor 1 and 8
L=100 cm, ø= 18 cm
one end cap only
n.28 17’’ glass spheres
Net buoyancy ~800 kg

## Slide 27
Backbone
Electro-optical cable
2 f.o. + 5 twisted pairs
Upper Floor
Lower Floor
Floor break out vessel
(equi-pressure oil bath)
Floor vessel
(in air)
Electrical cable
12 wires 18 AWG
V=375 V
Optical cable
2 optic fib.
the backbone

## Slide 28
the anchor
Schematic working principle
The interlink cable to the JB
1 laser beacon+ acoustic (Valencia, Gandia)
1 acustic beacon for LB positioning
2 hydrophones (monitor)

## Slide 29
PMT DAQ Boards
PMT DAQ Boards
Hydrophones DAQ Board
GPS receiver
Ethernet Floor Control Module
Floor Control Module
On-Shore
Off-Shore
Slow Control Interface
the floor electronics
100 km
28/10/12
Antonio Capone - LNS User Meeting

## Slide 30
Power supply & currents on each floor
Voltage 12 V
Current @12 V
Voltage 5 V
Currents @5 V
Total consumption on each floor (4 PMTs) ~ 17 Watt
Power consumption

## Slide 31
The DAQ system

## Slide 32
The tests
Power supply
To shore electronics
Configuration
Floors easy accesible in
the test Lab at the harbour
Light shielding on all PMTs
Interlink cable connected to:
-Power supply
-Optical link to shore station
DAQ to register PMT hits
Laser light source + optic fibres to OMs for timing measurements

## Slide 33
Background on single PMT @ nominal power supply
Rates around 5-8 kHz at nominal threshold (1/3 pe):
light shield not 100% effective
1 pe peak
Raw data only:
1 pe peak expected at
ch~100

## Slide 34
time calibration with laser light source
0
1
3
2
laser light source
Tunable frequency
Tunable amplitude
Illumination on horizontal PMT of the same floor
Laser source

## Slide 35
L1 trigger
Dt= 20 ns
Floor (true) coincidences
Simple (random) coincidences
Charge over threshold
coincidences

## Slide 36
Ambient noise on the Hydrophones
Floors 1-6 (except 5):
Smid TR401
Floor 7:
Senso Technologies LTD SX 30
(from Valencia, Gandia)

## Slide 37
Test of main electro optical cable at the Capo Passero shore station
Optical loss in 100 km cable: ~ 20 dB
P1-P3: the 3 connectors
in the cable termination

## Slide 38
Optimizations
Discussion on
mechanical structure
        >Fix PMT (Hamamatsu R7081)
        Fix OM housing >Fix n. of OM /floor (6) Fix design of the floor >Fix the distance of floor (30 m) >Fix the number of floors (14)
Update of the read out electronics
-FRONT END MODULE -simplified Front-end board, low power (<1W), reduced dimension (3"x3.5"), low cost; -analog sampling: ADC 200MHz@14bit (same performance, simpler design); -FLOOR CONTROL MODULE - Vessel electronics in 2 boards: power and logic; - low power consumption: ~6W, including DWDM Laser, instrumentation, hydro, compass;

## Slide 39
the new backbone
From daisy chain …
Floor N
Floor N+1
Floor N-1
SEACON cable : 2 optic fibres + 2 e.conductors
Delivered by November:
-1000 m to test attenuation during unfurling
-600 with 2 opt. connectors to test @ 400 bar
to point to point connection

## Slide 40
New design of the base of the tower
Will be the same as in the JB:
3 vessel + 1 manyfold
1 vessel to host optic fibres routing;
1 vessel for control ;
1 vessel for the power system in equipressure oil bath;
Improved reliability

## Slide 41
The deployment
planned at the end of the integration&tests by October 20th;
operated under MECMA consortium agreement: can be stopped according to a long list of «Interruptible Works»;
Predive check of the ROV underway ;
Single operation: CERTAMEN + ROV + tower:
              Test of the ROV at 3500 m and cable termination inspection.
              Deployment &connection of the tower

## Slide 43
The Great effort spent by INFN in the last 15 years finally is close to give the first results
A big European effort is pushing for the construction of the Km3 scale Neutrino Telescope in the Mediterranean Sea
PON funds allow for the construction of a first part of the Telescope
The 8 floors tower is completed and ready for the deployment, it will allow the final Tower detector concept validation
Extensive tests gave positive results
ROV dive test + deployment in the site of Capo Passero is planned by 2nd November .
Design optimisation process completed by end of the year
SUMMARY